**Camera/depth/registered/points	point cloud
|
|
find grasps	-look for possible grasps in a point cloud
point cloud clicker	-checks if the point cloud is received for it to	continue with the process
grasps sampler	-checks if the point cloud is received for it to	continue with the process

**camera/rgb/image_raw	rgb image
|
|
ClickedImageClient	-makes the rgb interactive obtaining clicked pixel	coordinate. Then it sends that coordinate as an	action goal to point_cloud_clicker.

Pixel coordinate Goal	x and y coordinate
|
|
point_cloud_clicker	-receives pixel coordinate and looks for points in	the point cloud that correspond to that pixel. Then it	sends another goal to find_grasps containing point	position in space and the workspace boundaries	around this point in which grasps will be found.

Point position Goal	point position & workspace boundaries (10 cm3)
|
|
find_grasps	-calculates possible grasps whithin the workspace	boundaries with the AGILE code. Publishes a list of	grasps.

List of grasps
|
|
grasps_sampler	-evaluates list of grasps and filter them with the	heuristic evaluator. Publishes a list of heuristic	modified grasps.

List of heuristic modified grasps
|
|
point_and_click	-interactive marker server which will locate a	gripper hand at the grasp location. This will also	send the position of the gripper as a goal for a real	robot arm to execute the grasps by going to the	indicated location.